ACID Install Instructions
For Version 0.7 of ACID

ACID is a custom version of Centos 5.2 with all the necessary support to run with a single USB fob on Allstar link.

Pre-Installation Notes

First, burn a CD by downloading the ISO CD image from http://dl.allstarlink.org.

WARNING: The CD will write over the current contents of the disk. Be sure that you have saved everything which needs saving before doing this install.

You will need an assigned Allstar link node number as it is required to complete the installation process. Allstar node numbers can be requested from http://allstarlink.org. In order to complete the installation, you will need your assigned allstar node number and the password. Please make a note of these when you receive email confirmation from allstarlink.org.

To install:

1. Connect the PC you are going to install to the your home network network making sure your home network has a DHCP server (Most consumer grade routers do).
2. Modify the BIOS settings on the PC to boot from CDROM first
3. Insert the CDROM in this package into the PC's CDROM drive, and force a reboot.
4. Press return when prompted
5. Wait for the installer to repartition and format the hard drive and install Centos.
6. When the installer puts up the reboot prompt, remove the CDROM and press enter.
7. Plug in your USB FOB if you haven't already
8. The system will now reboot and then proceed to install the rest of the software over the network.
9. After 2 more reboots, a prompt to change the root password will be displayed.
10. Follow the instructions, and change your root password, enter your node number, and your callsign for the identifier. The system will go down for a final reboot once this information is completely entered.

Post Installation Notes

Please note that the file /etc/ssh/sshd_config is configured to listen on port 222, and probably that should be changed to some other port number for added security.

The USB fob LED should be flashing once the system is completely booted. Now, the radio should be interfaced and the audio levels adjusted using the USB FOB setup procedures located at http://app-rpt.qrvc.com.

There are several helper scripts located in /root/acid. See the ACID system administration manual for further information.

Out of the box, ACID does not report status to http://stats.allstarlink.org. To enable status reporting,
add these two lines to the end of your node number definition e.g. [1234] in /etc/asterisk/rpt.conf:

statpost_program=/usr/bin/wget,-q,--output-document=/dev/null
statpost_url=http://stats.allstarlink.org/uhandler.php